## Slide 1
Source: https://lingojam.com/StephenHawkingVoiceGenerator

## Slide 2: Final Presentation of Advanced Seminar
Hannes Bohnengel
Technical University of Munich
TUM Department of Electrical and Computer Engineering
Chair of Real-Time Computer Systems
Munich, 21 July 2017

## Slide 3
The Impact of Deep Learning on Speech
Synthesis with Mobile Devices

## Slide 4: Outline
Content of Paper
Speech Synthesis in General
Introducing Deep Learning Models
Speech Synthesis on Mobile Devices
Conclusions

## Slide 5: Content of Paper
Intro
Conventional Speech Synthesis
  Motivation and Approaches
  HMM-based Synthesis  one paper
SPSS with Deep Learning Models
  One specific approach  one paper
  Asdf  one paper
Asdf
  Asdf  one paper
  Asdf  one paper
Conclusions

## Slide 6: Typical Applications of Speech Synthesis
Navigation Systems
Telephone-based Dialogue Systems
Reading Aid
Voice Communication Aid
(Stephen Hawking)
Communication in Air Traffic
Public Announcements
Virtual Assistants
Voice cloning
Speech-to-Speech Translation

## Slide 7: Types of Speech Synthesis
Source: Own visualization
Speech Synthesis
Canned Speech
Context-to-Speech (CTS)
Text-to-Speech (TTS)
Asdf
Asdf
Asdf
Asdf
Asdf
Asdf
Notes: CTS: the waveform is generated out of a linguistic description without any information of the respective text.
 No natural language processing is required, but nevertheless CTS has not made any important impact yet

## Slide 8: Text-to-Speech – Overview
Natural Language Processing
Part-of-speech tagging
Text normalization
Phonetic transcription
Syllabification
Stress prediction
Prosodic analysis
Front-end
Digital Signal
Processing
Depends on synthesis model
  Parametric
  Concatenative
  Statistical parametric
Back-end
Source: Boroș et al. (2015) Robust deep-learning models for text-to-speech synthesis support on embedded devices, Proceedings of the 7th
International Conference on Management of Computational and Collective intElligence in Digital EcoSystems (MEDES ’15)
Notes: Prosody is concerned with those elements of speech that are not individual phonetic segments (vowels and consonants) but are properties of syllables and larger units of speech. (e.g. pitch, loudness, length of sounds)
Text normalization is the process of transforming text into a single canonical form that it might not have had before.
The first text processing task we consider is syllabification: the decomposition of words into their phonological units.
The phonetic transcription task refers to the process of “translation” from letters to phonemes, an essential step in any TTS synthesis pipeline (also known as letter-to-sound or grapheme-to-phoneme translation)
Part-of-speech (POS) tagging is the process of assigning each word in a sentence its uniquely interpretable tag - its part of speech. A word’s POS (among other features) is used as a feature in the synthesis model, determining how the word is spoken.  choose the correct pronunciation for a homophone word
Lexical stress prediction: Certain syllables inside a word have a higher prominence compared to its neighboring syllables, giving the word a specific sound. Lexical stress prediction is essential in prosody generation, as it allows TTS systems to correctly choose pronunciations of homographs

## Slide 9: Text-to-Speech – Function blocks
Acoustic Model
Text
Text Analysis
Parameter Generation
Waveform Synthesis
Speech Parameters Trajectories
Speech
Front-end
Back-end
Context Features
Phoneme
Syllable
Word
Phrase
Utterance
Acoustic Features
Spectral Parameters
Excitation Parameters
Source: Own visualization
Notes: Context Features:
phoneme:
current phoneme
preceding and succeeding two phonemes
syllable:
- numbers of phonemes within preceding, current, and succeeding syllables
stress and accent of preceding, current, and succeeding syllables
word:
- guess at part of speech of preceding, current, and succeeding words
- numbers of syllables within preceding, current, and succeeding words
phrase:
- numbers of syllables within preceding, current, and succeeding phrases
- position of current phrase in major phrases
utterance:
- numbers of syllables, words, and phrases in utterance
Acoustic Features:
Spectral parameters: Mel-cepstral coefficients and their dynamic features
Excitation parameters: log F0 values and their dynamic features
mel-frequency cepstrum (MFC) is a representation of the short-term power spectrum of a sound, based on a linear cosine transform of a log power spectrum on a nonlinear mel scale of frequency.

## Slide 10: Text-to-Speech – Synthesis Models
Technique | Advantages | Drawbacks
Formant-based (Parametric) | Very small footprint | Very artificial and metallic voice
Unit-selection (Concatenative) | Very high voice quality possible | Large database required
HMM-based (Statistical parametric) | Adjustable voice and small footprint | Voice sounds muffled
Source: Own visualization
Table 1: Comparison of different speech synthesis techniques
Notes: The model is parametric because it describes the speech using parameters, rather than stored exemplars.
It is statistical because it describes those parameters using statistics (e.g., means and variances of probability density functions) which capture the distribution of parameter values found in the training data.
We can easily change voice characteristics, speaking styles, and emotions in statistical parametric synthesis by transforming its model parameters.
Four major techniques to accomplish this: adaptation, interpolation, eigenvoice, and multiple regression.

## Slide 11: Demonstration of HMM-based speech synthesis
Source: http://flite-hts-engine.sp.nitech.ac.jp/index.php

## Slide 12: Outline
Speech Synthesis in General
Introducing Deep Learning Models
Speech Synthesis on Mobile Devices
Conclusions

## Slide 13: Introducing Deep Learning Models
Source: Zen et al. (2013) Statistical parametric speech synthesis using deep neural networks, IEEE International Conference on Acoustics, Speech and Signal Processing
Figure 1: DNN as acoustic model
Acoustic Model
Context
Features
Acoustic
Features
Notes: Using a Deep Neural Network (DNN) as acoustic model
Only modification in Back-end

## Slide 14: Results of Experiments
Objective evaluation
DNN-based systems have less distortion
HMM-based systems have a lower error rate in some cases
Subjective evaluation
 DNN-based systems are preferred
 Described as less muffled
HMM-based (scaling factor) | DNN-based (neurons per layer) | Neutral
15.8 % (16) | 38.5 % (256) | 45.7 %
16.1 % (4) | 27.2 % (512) | 56.8 %
12.7 % (1) | 36.6 % (1024) | 50.7 %
Table 2: Subjective scores
Source: Zen et al. (2013) Statistical parametric speech synthesis using deep neural networks, IEEE International Conference on Acoustics, Speech and Signal Processing
Notes: The DNN-based systems consistently outperformed the HMM-based ones in voiced/unvoiced classification and aperiodicity prediction. The DNN-based systems with many layers were similar to or better than the HMM-based ones in Mel-cepstral distortion. On the other hand, the HMM-based systems outperformed the DNN-based ones in log F0 prediction in most cases.
the DNN-based systems were preferred significantly to the HMM-based ones in all three model sizes. The subjects reported that the DNN-based systems were less muffled.
The authors expect that better prediction of Mel-cepstral coefficients by the DNN-based systems contributed to the preference.

## Slide 15: Outline
Speech Synthesis in General
Introducing Deep Learning Models
Speech Synthesis on Mobile Devices
Conclusions

## Slide 16: One Approach to Decrease the Footprint Size
Introducing a DNN into the front-end of a TTS-System
Syllabification (SYL)  extraction of syllables
Phonetic transcription (PT)  extraction of phonemes
Part-of-speech tagging (POT)  assigning each word a unified tag
Lexical stress prediction (LSP)  decision if to stress a syllable
Notes: Syllabification: the decomposition of words into their phonological units.
Phonetic transcription: the process of “translation” from letters to phonemes (also known as letter-to-sound or grapheme-to-phoneme translation)
Part-of-speech (POS) tagging is the process of assigning each word in a sentence its uniquely interpretable tag - its part of speech.
choose the correct pronunciation for a homophone word
N: Nouns V: Verbs A: Adjectives R: Adverbs
feminine/maskular, singular/plular, cases
Lexical stress prediction: Certain syllables inside a word have a higher prominence compared to its neighboring syllables, giving the word a specific sound.
 choose the correct pronunciation for a homophone word

## Slide 17: Results of Experiments
Overall reduction of model size by ~ 60 %
Table 3: Resulting accuracy and footprint size
Source: Boroș et al. (2015) Robust deep-learning models for text-to-speech synthesis support on embedded devices, Proceedings of the 7th
International Conference on Management of Computational and Collective intElligence in Digital EcoSystems (MEDES ’15)
 | SYL |  | PT |  | POT |  | LSP | 
 | Con. | DNN | Con. | DNN | Con. | DNN | Con. | DNN
Accuracy | 99.01 % | 98.23 % | 96.29 % | 96.16 % | 98.19 % | 95.16 % | 98.80 % | 97.67 %
Size | 9.4 MB | 36.7 KB | 1.4 MB | 43.4 KB | 96 MB | 178 KB | 6 MB | 110 KB
Con. = Conventional
Notes: Tremendous reduction of footprint size
Accuracy not significantly decreased
As reference system, the Margin Infused Relaxed Algorithm (MIRA) is used.

## Slide 18: Outline
Speech Synthesis in General
Introducing Deep Learning Models
Speech Synthesis on Mobile Devices
Conclusions

## Slide 19: Conclusions
Introduction of deep learning models into speech synthesis
Better voice quality
Smaller memory footprint
Huge increase of available smartphones expected
Need for robust and resource-efficient implementations
Deep learning models can be used to achieve this
Speech sample

## Slide 20: Thank you for your attention!

## Slide 21: Speech Synthesis on Mobile Devices
Mobile devices
Real-time responsiveness
Memory constraints
Power consumption
Notes: Speech as extension
Speech as main output
Help visually impaired or blind people

## Slide 22: HMM-based Speech Synthesis Model
Source: Black et al. (2007) Statistical Parametric Speech Synthesis,
IEEE International Conference on Acoustics, Speech and Signal Processing - ICASSP ’07

## Slide 23: HMM-based Speech Synthesis
Instance of Statistical Parametric Speech Synthesis (SPSS)
Context-dependent Hidden Markov Models (HMMs) as acoustic model
Decision-tree-based mapping from context features to acoustic features
Adjustable voice characteristics
Best trade-off between footprint size and voice quality
Voice still sounds muffled  Further improvement necessary
Notes: Training and Synthesis Part
generating the average of some sets of similarly sounding speech segments.
(Decision Trees / (Maximum Likelyhood Parameter Generation) )
Training:
both spectrum (e.g., mel-cepstral coefficients and their dynamic features) and excitation (e.g., log F0 and its dynamic features) parameters are extracted from a database of natural speech and modeled by a set of multi-stream context-dependent HMMs
linguistic and prosodic contexts are taken into account in addition to phonetic ones
Synthesis:
word sequence is converted into a context dependent label sequence
utterance HMM is constructed by concatenating the context-dependent HMMs according to the label sequence
the speech parameter generation algorithm generates the sequences of spectral and excitation parameters from the utterance HMM
speech waveform is synthesized from the generated spectral and excitation parameters using excitation generation and a speech synthesis filter

## Slide 24: Context Features
phoneme:
- current phoneme
- preceding and succeeding two phonemes
- position of current phoneme within current syllable
syllable:
- numbers of phonemes within preceding, current, and succeeding syllables
- stress and accent of preceding, current, and succeeding syllables
- positions of current syllable within current word and phrase
- numbers of preceding and succeeding stressed syllables within current phrase
- numbers of preceding and succeeding accented syllables within current phrase
- number of syllables from previous stressed syllable
- number of syllables to next stressed syllable
- number of syllables from previous accented syllable
- number of syllables to next accented syllable
- vowel identity within current syllable
word:
- guess at part of speech of preceding, current, and succeeding words
- numbers of syllables within preceding, current, and succeeding words
- position of current word within current phrase
- numbers of preceding and succeeding content words within current phrase
- number of words from previous content word
- number of words to next content word
phrase:
- numbers of syllables within preceding, current, and succeeding phrases
- position of current phrase in major phrases
- ToBI endtone of current phrase
utterance:
- numbers of syllables, words, and phrases in utterance
Source: Black et al. (2007) Statistical Parametric Speech Synthesis, IEEE International Conference on Acoustics, Speech and Signal Processing - ICASSP ’07

## Slide 25: Acoustic Features
Spectral parameters: Mel-cepstral coefficients and their dynamic features
Excitation parameters: log Fo values and their dynamic features